## Slide 1
BUY AMERICA OVERVIEW
Edwin T. Okonkwo
Construction Team HICP-20
FHWA Office of Infrastructure
Unless otherwise noted, FHWA is the source for all images in this presentation.

## Slide 2: Disclaimer
Except for any statutes or regulations cited, the contents of this presentation do not have the force and effect of law and are not meant to bind the States or the public in any way. This presentation is intended only to provide regarding existing requirements under the law or agency policies.
Notes: General disclaimer to let participants know that the contents of the presentation do not have the force and effect of law. Is only intended to provide information to the public on existing requirements under the law or agency policies.

## Slide 3: FHWA’s Buy America Regulatory Requirements 23 CFR 635.410
Apply to iron and steel materials and products only
  all manufacturing processes must take place domestically, including the application of a coating on these materials
Minimal use provision (greater of 0.1% of contract value or $2,500)
Optional alternate bid provision (25% differential)
Waivers may be requested if:
  Applying requirements would be inconsistent with the public interest; or
  Domestically produced steel and iron are not produced in sufficient and reasonably available quantities which are of a satisfactory quality
Notes: Cleared 12/1/22
FHWA’s BA regulations in 23 CFR 635.410 apply to iron and steel materials only. All manufacturing processes must take place domestically, including the application of coating on the materials.

## Slide 4: Application of Buy America Preference
SEC. 70914 of the Bipartisan Infrastructure Law (BIL) (Pub. L. No. 117-58)
(a) IN GENERAL.—Not later than 180 days after the date of enactment of this Act, the head of each Federal agency shall ensure that none of the funds made available for a Federal financial assistance program for infrastructure, including each deficient program, may be obligated for a project unless all of the iron, steel, manufactured products, and construction materials used in the project are produced in the United States. (emphasis added)
Buy America requirements = 23 USC 313 + BABA; iron, steel, manufactured products, and construction materials.
Notes: Cleared 12/1/22
In General, section 70914 of the BIL requires the application of Buy America to all of the iron, steel, manufactured products and construction materials.

## Slide 5: Bipartisan Infrastructure Law – Build America, Buy America Act (BABA) (BIL, div. G, § 70901-27)
BABA Section 70914 includes a Buy America preference that all Federal agencies must apply to any Federal financial assistance program for infrastructure that is not already subject to existing Buy America requirements for the relevant categories.
BABA Section 70917(a) provides that the Buy America requirements under Section 70914 apply only to the extent that Federal agencies do not already apply a Buy America preference to steel, iron, manufactured products, and construction materials.
  This provision allows FHWA to preserve existing Buy America policies and provisions that meet or exceed the standards required by BABA, such as its requirements for iron and steel under 23 U.S.C. 313, and only extends coverage of Buy America to “construction materials.”
Notes: Cleared 12/1/22
Section 70917(a) provide that sec 70914 apply only to the extent that Federal agencies do not already apply a Buy America preference to iron, steel, manufactured products, and construction materials.
FHWA already applies Buy America requirements in 23 U.S.C. 313 and 23 CFR 635.410 to Federal-aid programs for iron and steel products and FHWA’s manufactured products general waiver covers manufactured products. BABA Section 70917(a) allows FHWA to preserve requirements for iron and steel and manufactured products. Only construction materials need to be covered.

## Slide 6: What is a Construction Material?
According to the preliminary and non-binding guidance in U.S. Office of Management and Budget (OMB) Memorandum, M-22-11, “Construction materials” includes an article, material, or supply — other than an item of primarily iron or steel; a manufactured product; cement and cementitious materials; aggregates such as stone, sand, or gravel; or aggregate binding agents or additives — that is or consists primarily of:
non-ferrous metals;
plastic and polymer-based products (including polyvinylchloride, composite building materials, and polymers used in fiber optic cables);
glass (including optic glass);
lumber; or
drywall.
Notes: Cleared 12/1/22

## Slide 7: Construction Materials (cont’d.)
Items excluded from construction materials under OMB Memo M-22-11:
An item of primarily iron or steel
A manufactured product
Cement and cementitious materials
Aggregates such as stone, sand, or gravel
Aggregate binding agents or additives
Asphalt concrete pavement mixes are typically composed of asphalt cement (a binding agent) and aggregates such as stone, sand, and gravel. Accordingly, asphalt is also excluded from this definition of the term construction materials.
Notes: Cleared 12/1/22

## Slide 8: Construction Materials (cont’d.)
Pending issuance of final standards from OMB, agencies should consider “all manufacturing processes” for construction materials to include at least the final manufacturing process and the immediately preceding manufacturing stage for the construction material. See OMB Memorandum M-22-11 of April 18, 2022.
Notes: Cleared 12/1/22

## Slide 9: OMB Final Guidance (2 CFR 200
On August 23, 2023, OMB published in the FR a final guidance; https://www.federalregister.gov/public-inspection/2023-17724/guidance-for-grants-and-agreements for Buy America Act provisions of the Infrastructure Investment and Jobs Act and to clarify existing provisions related to domestic preferences. Effective date is 60 days from date of publication.
Establishes new part 184 under 2 CFR 200 for determining the cost of components of manufactured products.
Agencies/State DOTs to implement the Buy America preferences set forth in 2 CFR part 184, as required under section 70914(a) BABA, as of the effective date of the guidance, unless specified otherwise.

## Slide 10: OMB Final Guidance contd.
Section 184.4: Categorization of Articles, Materials, and Supplies
  Iron and steel
  Manufactured product
  Construction material
  Materials
  Decision made based on the statute at the time it is brought to work site for incorporation.
Section 184.6: Construction material standards
  Non-ferrous metals: all manufacturing process means melting through final shaping, coating and assembly occurred in U.S.

## Slide 11: Construction materials standard contd.
  Plastic and Polymer-based products: All manufacturing processes, from initial
  combination of constituent plastic or polymer-based inputs, or, where applicable, constituent
  composite materials, until the item is in its final form, occurred in the United States
Glass: All manufacturing processes, from initial batching and melting of raw materials through annealing, cooling, and cutting, occurred in the United States.
Lumber: All manufacturing processes, from initial debarking through treatment and planing, occurred in the United States.
Drywall: All manufacturing processes, from initial blending of mined or synthetic gypsum plaster and additives through cutting and drying of sandwiched panels, occurred in the United States

## Slide 12: Waiver for De Minimis Costs, Small Grants, and Minor Components
On August 16, USDOT finalized the Public Interest Waiver for De Minimis Costs and Small Grants: https://www.federalregister.gov/documents/2023/08/16/2023-17602/waiver-of-buy-america-requirements-for-de-minimis-costs-and-small-grants.
The public interest waiver is for projects funded under DOT-administered financial assistance programs for iron, steel, manufactured products, and construction materials under a single financial assistance award for which:
The total value of the non-compliant products is no more than the lesser of $1,000,000 or 5% of total applicable costs for the project*; or
The total amount of Federal financial assistance applied to the project, through awards or subawards, is below $500,000.
*This bullet does not apply to iron and steel subject to the requirements of 23 U.S.C. 313 on financial assistance administered by FHWA. The de minimis threshold in 23 CFR 635.410(b)(4) continues to apply for steel and iron.

## Slide 13: Waiver for De Minimis Costs, Small Grants, and Minor Components
The waiver is applicable only to awards that are obligated or subawards that are made on or after the effective date of the waiver, August 16, 2023. The waiver is applicable to subawards only if the subawards are made by a pass-through entity for a specific project. Electric Vehicle (EV) chargers continue to be subject to the FHWA Buy America EV Charger Waiver.

## Slide 14: FHWA General Waiver for Manufactured Products
FHWA’s general waiver for manufactured products remains in effect. Because FHWA has an existing statutory requirement applicable to manufactured products, the BABA standard for manufactured products under Section 70912(6)(B) does not apply on Federal-aid highway projects.
BABA Section 70914(d) provides a process for reviewing existing waivers of general applicability, such as FHWA’s general waiver for manufactured products.
Notes: Cleared 12/1/22
FHWA’s general applicability waiver for manufactured products remain in effect. However BABA Section 70914(d) requires FR reviews every 5 years (for first 5 years, does not apply to any product-specific waivers of general applicability issued more than 180 days before November 15, 2021)

## Slide 15: FHWA General Waiver for Manufactured Products (cont’d)
Pursuant to BABA Section 70914(d), the FHWA published a notice in the Federal Register on March 17, 2023, seeking comments on its existing general applicability waiver for manufactured products under its Buy America waiver authorities (88 FR 16517).
The comment period was extended to end on May 22, 2023 (88 FR 24651). Over 9400 comments were received.
Following review and consideration of comments, FHWA will publish a determination on whether to continue, discontinue, or otherwise modify the waiver and will consider other actions related to the implementation of Buy America requirements for manufactured products.
Notes: *Updated slide*

## Slide 16: FHWA’s Existing General Applicability Waivers
Per BABA Section 70914(d), all existing general applicability waivers shall be reviewed in the Federal Register every 5 years after the date on which the waiver is issued.
FHWA has four general applicability waivers:
  Manufactured products
  Pig Iron and Processed, Pelletized, and Reduced Iron Ore
  Ferryboat parts
  Concrete poles for Guam
Notes: Cleared 12/1/22
OMB memo M-22-11 reaffirmed reviews of all existing non-product specific general applicability waivers. FHWA has four general applicability waivers: manufactured product waiver; pig iron and processed, pelletized, and reduced iron ore; ferryboats; and concrete poles for Guam.

## Slide 17: EV Charger Waiver (88 FR 10619)
Published in the Federal Register on February 21, 2023; effective date was March 23, 2023.
This short-term, temporary public-interest waiver enables EV charger acquisition and installation to immediately proceed while also ensuring the application of Buy America to EV chargers by the phasing out of the waiver over time.
Starting on March 23, 2023, FHWA removed EV chargers from being covered by its Manufactured Products General Waiver
Phase I: Waiver of 23 U.S.C. 313(b)(1), 23 CFR 635.410(c), and Section 70914(b) of BABA to EV chargers and all components of EV chargers if final assembly occurs in the U.S. for all chargers that are manufactured from the effective date of the waiver until June 30, 2024. Installation must begin by October 1, 2024.
Phase II: Starting on July 1, 2024, waiver will only cover EV chargers if final assembly occurs in the U.S. and if the cost of components manufactured in the U.S. exceeds 55% of the cost of all components.
Both phases: All predominately steel and iron housing components are excluded from the waiver and must comply with FHWA’s existing Buy America requirements for steel and iron.
BABA Implementation Plan to Enhance Buy America for EV Chargers Q&As posted on the FHWA website on July 11, 2023 (https://www.fhwa.dot.gov/construction/contracts/buyam_qaev/)
Notes: *New slide*

## Slide 18: References
FHWA Buy America Construction Program Guide page: https://www.fhwa.dot.gov/buyamerica/
FHWA BABA Implementation Plan to Enhance Buy America for EV Chargers Q&As: (https://www.fhwa.dot.gov/construction/contracts/buyam_qaev/)
EV Charger Waiver: https://www.federalregister.gov/documents/2023/02/21/2023-03498/waiver-of-buy-america-requirements-for-electric-vehicle-chargers
OMB Proposed Guidance for Grants and Agreements: https://www.federalregister.gov/documents/2023/02/09/2023-02617/guidance-for-grants-and-agreements
Review of Manufactured Products Waiver: https://www.federalregister.gov/documents/2023/03/17/2023-05498/notice-and-request-for-comment-on-fhwas-review-of-its-general-applicability-waiver-of-buy-america
Notes: *Updated slide*

## Slide 19: Contacts
Edwin Okonkwo, Buy America Program Manager Edwin.Okonkwo@dot.gov, 202-366-1558
Brian Hogge, Construction Team Leader Brian.Hogge@dot.gov, 202-366-1562

## Slide 20: Questions? Thank you!